This guide specification is written according to the Construction Specifications Institute (CSI) formats, including MasterFormat, SectionFormat, and PageFormat.

Carefully review and edit this section to meet the requirements of the project and local building code. Coordinate this section with other specification sections and drawings.

Delete all "Specifier Notes" when done editing this section.

SECTION 26 05 33.16

TABLE BOXES FOR ELECTRICAL SYSTEMS

GENERAL

CONDITIONS AND REQUIREMENTS

The General Conditions, Supplementary Conditions, and Division 01 – General Requirements apply.

SECTION INCLUDES

Desktop power centers for power and charging.

RELATED SECTIONS

Specifier Note: In this article, specify work specified in other sections that is related to work of this section.

Division 26 - Electrical: Electrical systems and components.

Specifier Note: The following paragraph is a sample that may be used in this article.  Add to or delete from the following as appropriate for the specific project.

Section [xx xx xx] – [Section Title]: [Include brief description of work specified in another section that is related to the work of this section.]

SUBMITTALS

Specifier Note: In this article, specify various types of data to be furnished by the contractor before, during, or after construction. Topics included in this article are:  product data, shop drawings, samples, design data, test reports, certificates, manufacturers’ instructions, manufacturers’ field reports, qualification statements, and closeout submittals.

Submit under provisions of Section [01 33 00] [______].

Product Data: Submit for desktop power centers.

QUALITY ASSURANCE

Specifier Note: In this article, describe qualifications, regulatory requirements, certifications, field samples, mock-ups, and pre-installation meetings.

Manufacturer Qualifications: Firms regularly engaged in manufacture of desktop power centers of the types and sizes required, whose products have been in satisfactory use in similar service for not less than 10 years. Provide desktop power centers produced by a manufacturer listed in this section.

Source Limitations: Obtain each type of desktop power center through one (1) source from a single manufacturer.

Electrical Boxes and Fittings: Comply with requirements of applicable local codes, NEC, UL, ETL, and NEMA Standards pertaining to desktop power centers.

DELIVERY, STORAGE AND HANDLING

Deliver desktop power centers in factory labeled packages.

Store and handle in strict compliance with manufacturer’s written instructions and recommendations.

Protect from damage due to weather, excessive temperature, and construction operations.

PRODUCTS

ACCEPTABLE MANUFACTURERS

Basis-of-Design Product: The design for table boxes and fittings is based on the Desktop Power Center Slim manufactured by Legrand/Wiremold, 60 Woodlawn Street, West Hartford, CT 06110; toll-free 877-295-3472, telephone 860-233-6251, fax 860-232-2062; Web Site: www.legrand.us/wiremold.

Substitutions will be considered under provisions of Section 01 25 00.

DESKTOP POWER CENTERS

Classification and Use: Desktop power centers shall have been examined, tested and listed by ETL to US and Canadian Safety Standards.

Desktop Power Centers, General: Desktop power centers shall provide convenience outlets for power and USB charging.

Specifier Note: Retain one of the finish colors in the following paragraph and delete the other one.

Desktop Power Centers: cETLus Listed Furniture Power Distribution Box.  Service location above table; furnish with six (6) foot [1.83m] cord; color - [matte black housing and face] [gloss white housing with gray face].

Specifier Note: Retain one or more of the following subparagraphs as required for a project; delete those not required.

Desktop Power Centers:

Specifier Note: Retain one of the finish colors in the following subparagraphs and delete the other one.

Catalog No. WSPC220[BK][WH]; [black] [white] color; two (2) outlet unit which includes two (2) 15A tamper-resistant power receptacles and two (2) smart USB ports that provide 3.1 amps. Provide with screw in mounting plate for forward facing outlets.

Catalog No. WSPC320[BK][WH]; [black] [white] color; three (3) outlet unit which includes three (3) 15A tamper-resistant power receptacles and two (2) smart USB ports that provide 3.1 amps. Provide with screw in mounting plate for forward facing outlets.

Desktop Power Centers with Surge Protection:

Catalog No. WSC320BK; black color; three (3) outlet unit which includes three (3) 15A tamper-resistant power receptacles and two (2) smart USB ports that provide 3.1 amps. Provide with accessories for mounting into round cut-outs in desk or edge mounting on desks or other surfaces.

Alternate Mounting Kit for Desktop Power Centers:

Specifier Note: Retain one of the finish colors in the following subparagraph and delete the other one.

Catalog No. WSPC220BKT[BK][GY]; [black] [gray] finish; kit includes clamp for screwless mounting, and right-angle screw in mounting plate. Two-piece clamp allows the desktop power center to be installed against partition walls without dismantling them. Clamp allows outlets to be mounted forward or upward facing. Right-angle screw in mounting plate allows outlets to be mounted upward facing.

EXECUTION

EXAMINATION

Specifier Note: Retain one (1) of the options in the first paragraph below and delete the other one.

Examine conditions under which desktop power centers are to be installed. Notify the [Architect/Engineer] [Construction Manager] in writing of conditions detrimental to proper completion of the work. Do not proceed with work until unsatisfactory conditions have been corrected.

INSTALLATION

Strictly comply with manufacturer's installation instructions and recommendations. Coordinate installation with adjacent work to ensure proper clearances and to prevent electrical hazards.

CLEANING AND PROTECTION

Clean exposed surfaces using non-abrasive materials and methods recommended by manufacturer.

Protect desktop power centers until acceptance.

END OF SECTION

A copyright license to reproduce this specification is hereby granted to non-manufacturing engineers, architects and specification writers.

|  | Legrand / Wiremold U.S. and International: 60 Woodlawn Street ( West Hartford, CT 06110 1-877-295-3472 ( FAX: 860-232-2062 ( Outside U.S.: 860-233-6251 Canada: 570 Applewood Crescent ( Vaughan, Ontario L4K 4B4 1-800-723-5175 ( FAX: 905-738-9721 |
| --- | --- |
| (2019 Legrand/Wiremold All Rights Reserved | EDXXXX – New June 2019 – For latest specs visit www.legrand.us/wiremold |