Da-Lite®

3100 N. Detroit St.

Warsaw, IN 46582

Phone: (800) 622-3737

Phone: (574) 267-8101

Fax: (877) 325-4832

Fax: (574) 267-7804

E-mail: info@da-lite.com

www.da-lite.com

This MANU-SPEC® utilizes the Construction Specifications Institute (CSI) Project Resource Manual (PRM), including MasterFormat™, SectionFormat™ and PageFormat™. A MANU-SPEC is a manufacturer-specific proprietary product specification using the proprietary method of specifying applicable to project specifications and master guide specifications. Optional text is indicated by brackets [ ]; delete optional text in final copy of specification. Specifier Notes precede specification text; delete notes in final copy of specification. Trade/brand names with appropriate product model numbers, styles and types are used in Specifier Notes and in the specification text Article titled “Acceptable Material.” Metric conversion, where used, is soft metric conversion.

This MANU-SPEC specifies electrically operated motorized projector lifts as manufactured by Da-Lite® Screen Company, Inc. Revise MANU-SPEC section number and title below to suit project requirements, specification practices and section content. Refer to CSI MasterFormat for other section numbers and titles.

SECTION 11 52 16

PROJECTORS

GENERAL

SUMMARY

Section Includes: Electrically operated motorized projector lifts and related accessories for ceiling installation of multimedia projectors.

Specifier Note: Revise paragraph below to suit project requirements. Add section numbers and titles per CSI MasterFormat and specifier’s practice.

RELATED SECTIONS

Specifier Note: Include in this Paragraph only those sections and documents that directly affect the work of this section. If a reader of this section could reasonably expect to find a product or component specified in this section, but it is actually specified elsewhere, then the related section number(s) should be listed in the Subparagraph below. Do not include Division 00 documents or Division 01 sections since it is assumed that all technical sections are related to all project Division 00 documents and Division 01 sections to some degree. Refer to other documents with caution since referencing them may cause them to be considered part of the Contract.

Section [26 05 00 - Common Work Results for Electrical: Power supply, conduit and wiring] [______].

Section [______].

  - ADMINISTRATIVE REQUIREMENTS

    - Coordination: Coordinate work of this Section with work of other trades for proper time and sequence to avoid construction delays. Comply with Section [01 31 00 - Project Management and Coordination].

Specifier Note: Add additional text to specify unusual or detailed coordination requirements affecting the work results of this Section.

      - [______].

    - Sequencing: Sequence work of this section in accordance with Section [01 12 16 - Work Sequence] [and manufacturer(s written recommendations for sequencing construction operations].

Specifier Note: Specify additional text as required to describe the particular sequence of events required to coordinate work that must be done in sequence with, or at the same time as, work in another section.

      - [______].

    - Scheduling: Schedule work of this Section in accordance with Section [01 32 13 - Scheduling of Work].

Specifier Note: Specify additional text to include requirements for coordinating work that requires unusual scheduling with work of other sections.

      - [______].

Specifier Note: Article below includes submittal of relevant data to be furnished by Contractor before, during or after construction. Coordinate this article with Architect’s and Contractor(s duties and responsibilities in Contract Conditions and Section 01 33 00 - Submittal Procedures.

  - ACTION SUBMITTALS

    - General: Submit listed submittals in accordance with Contract Conditions and Section [01 33 00 - Submittal Procedures].

    - Product Data: Submit for specified products as follows:

      - Manufacturer's product data, including manufacturer(s technical data sheet(s).

      - Catalog pages illustrating products to be incorporated into project.

    - Shop Drawings: Indicate information on shop drawings as follows:

      - Layout indicating locations.

      - Dimensions.

      - Installation details.

      - Electric wiring diagrams.

      - Manufacturer’s recommendations for accessories.

      - [______].

  - INFORMATION SUBMITTALS

Specifier Note: Specify submittal of test reports or evaluation service reports intended to document required tests without repeating the test requirements specified in Division 01.

    - General: Submit listed submittals in accordance with Contract Conditions and Section [01 33 00 - Submittal Procedures].

    - Test and Evaluation Reports:

      - Certified test reports showing compliance with specified performance characteristics and physical properties.

      - Documentation verifying product UL and ULC listing.

Specifier Note: Specify submittals intended to document manufacturer installation, storage and other instructions.

    - Manufacturer(s Instructions: Submit manufacturer(s [storage] [and] installation instructions.

    - Source Quality Control: Submit documentation verifying that components and materials specified in this Section are from a single manufacturer.

Specifier Note: Coordinate with Field Quality Control in PART 3. When manufacturer(s services are specified during construction operations to verify installation, include the following Paragraph for submittal of instructions and reports. If no field inspections are required, delete the following Paragraph.

    - Qualification Statements:

      - Submit letter of verification for Manufacturer(s Qualifications.

      - Submit letter of verification for Installer(s Qualifications.

  - CLOSEOUT SUBMITTALS

    - General: Submit listed submittals in accordance with Contract Conditions and Section [01 33 00 - Submittal Procedures].

    - Operation and Maintenance Data:

      - Submit operation and maintenance data for installed products in accordance with Section [01 78 23 - Operation and Maintenance Data]. Include:

Specifier Note: Edit or expand list of operation and maintenance data submittal inclusions to suit project requirements.

        - Parts catalog giving showing complete list of available parts.

        - List of replacement parts with cuts and identifying numbers.

    - Warranty Documentation: Submit warranty documents specified.

  - QUALITY ASSURANCE

    - Qualifications:

      - Manufacturer:

        - [5] years of experience manufacturing components similar to or exceeding requirements of project.

        - Having sufficient capacity to produce and deliver required materials without causing delay in work.

        - Capable of providing field service representation during construction.

      - Installer: Acceptable to manufacturer, experienced in performing work of this section and having specialized in installation of work similar to that required for this project.

  - DELIVERY, STORAGE & HANDLING

    - Delivery and Acceptance Requirements:

      - Deliver material in accordance with Section [01 61 00 - Common Product Requirements] and in accordance with manufacturer(s written instructions.

      - Deliver materials in manufacturer(s original packaging with identification labels intact and in sizes to suit project.

    - Storage and Handling Requirements:

      - Store materials protected from exposure to harmful weather conditions and at temperatures recommended by manufacturer.

    - Packaging Waste Management:

Specifier Note: The disposal of packaging waste into landfill sites demonstrates an inefficient use of natural resources and consumes valuable landfill space. Specifying appropriate packaging and construction waste management and disposal procedures may contribute to points required for USGBC(s LEED® construction project certification.

Specifier Note: Include the following Subparagraphs to specify information that will provide direction to the Contractor for the disposal of construction waste materials using environmentally responsible methodology other than landfill resources.

      - Separate waste materials for [reuse] [and] [recycling] in accordance with Section [01 74 19 - Construction Waste Management and Disposal].

Specifier Note: USGBC(s LEED® certification includes credits for the diversion of construction waste from landfill. Diversion can be tracked by either weight or volume but must be consistent for all materials. Manufacturer may reclaim packaging and delivery materials for recycling.

      - Remove packaging materials from site and dispose of at appropriate recycling facilities.

      - Collect and separate for disposal [paper] [plastic] [polystyrene] [corrugated cardboard] packaging material [in appropriate onsite bins] for recycling.

      - Fold metal and plastic banding, flatten and place in designated area for recycling.

Specifier Note: Add additional Subparagraphs to include pallets, crates, padding and other packing materials that are typically associated with the specified products.

      - Remove:

        - Pallets from site [and return to supplier or manufacturer].

        - [______].

PRODUCTS

MANUFACTURERS

Specifier Note: Retain Article below for proprietary method specification. Add product attributes, performance characteristics, material standards and descriptions as applicable. Use of such phrases as “or equal,” “or approved equal” or similar phrases may cause ambiguity in specifications. Such phrases require verification (procedural, legal and regulatory) and assignment of responsibility for determining “or equal” products.

Manufacturer: Da-Lite Screen Company, Inc.

Contact: P.O. Box 137, 3100 N. Detroit St., Warsaw, IN 46581-0137; Telephone: (800) 622-3737, (574) 267-8101; Fax: (877) 325-4832, (574) 267-7804; E-mail: info@da-lite.com; website: www.da-lite.com.

Single Source Responsibility: Provide components and materials specified in this section from a single manufacturer.

Specifier Note:  Substitution procedures must either be in Contract Conditions or in Section 01 25 00 - Substitution Procedures. Do not include substitution procedures here.

Substitution Limitations:

Substitutions: [In accordance with [Contract Conditions] [Section 01 25 00 - Substitution Procedures]] [No substitutions permitted].

Specifier Note: Two types of motorized projector lifts for recessed ceiling installations are described in this Section. The first is a pivot-type, which has a fixed pivot point design to help properly align the projector during and after installation. The second type is a non-pivoting system. Refer to manufacturer’s technical data sheets and retain or delete Pivot Type or Non-Pivot Type articles. Edit bracketed information to suit project requirements.

PIVOT-TYPE MOTORIZED PROJECTOR LIFT

General Requirements:

Specifier Note: Paragraph below should list obligations for compliance with specific code requirements particular to this section. General statements to comply with a particular code are typically addressed in Contract Conditions and Section 01 41 00 - Regulatory Requirements. Repetitive statements should be avoided.

Regulatory Requirements:

In accordance with Section [01 41 00 - Regulatory Requirements].

[______].

Compatibility:

Verify that components and materials are compatible with specified accessories and adjacent materials.

Performance Criteria:

Capacity: To 25 lb (11 kg), maximum.

UL and ULC listed.

Specifier Note: Standard operation of pivot-type projectors by Da-Lite Screen Co., Inc., is via wall-mounted push-button control. Remote control operation is also available as an option. Refer to manufacturer’s product information and technical data, and retain or delete bracketed information below to suit project requirements.

Operation:

Operator: 12 V DC linear actuator.

Voltage, Frequency: 120V, 60 Hz.

Amperage: 5, maximum.

Electrical Controls: Provide the following:

Receptacle: Prewired 120V AC grounded duplex type.

Switch: Prewired push-button type with cover plate for UP, DOWN and STOP functions.

Low Voltage Control (LVC) System: Single motor type.

Materials: Provide motorized projector mount constructed of the following:

Frame: Fabricated mild steel.

Support Frame: 14 gauge welded steel.

Tilting Frame: 14 gauge welded steel.

Ceiling Tile Holder: 18 gauge welded steel.

Ceiling Tile Trim: 18 gauge welded steel.

Finish: Powder coated white.

Accessories:

Key Locking Cover Plate: Hinged cover plate with brushed stainless steel finish for keyed access to LVC wall switch.

Specifier Note: Specify wireless remote control with either radio frequency or infrared operation to suit project requirements.

Wireless Remote Control for LVC: [Radio frequency remote [with frequency range extender]] [Infrared] 3-button handheld remote control for UP, DOWN and STOP functions. Plenum Kit:

Specifier Note: Refer to manufacturer’s product and technical data, and specify plenum kit model and description to suit project requirements.

Plenum Kit:

Model, Description: [______] [As recommended by manufacturer].

Specifier Note: Pivot-type recessed motorized projector lifts by Da-Lite Screen Co., Inc., are available in two standard models for suspended or drywall ceiling installation. Refer to manufacturer’s product information and technical data, and retain or delete paragraph(s) below to suit project requirements.

Da-Lift Pivot Motorized Video Projector Lift Model 26P:

Dimensions:

Rear Width: 17 inches (432 mm).

Height: 13.63 inches (346 mm).

Outside Depth: 25.38 inches (645 mm).

Front Width: 16 inches (406 mm).

Inside Depth: 14 inches (356 mm).

Pivot Depth: 12.75 inches (324 mm).

Da-Lift Pivot Motorized Video Projector Lift Model 33P:

Dimensions:

Rear Width: 21.5 inches (546 mm).

Height: 16.63 inches (422 mm).

Outside Depth: 32.38 inches (822 mm).

Front Width: 20.5 inches (521 mm).

Inside Depth: 18.5 inches (470 mm).

Pivot Depth: 16.25 inches (413 mm).

NON-PIVOT TYPE MOTORIZED PROJECTOR LIFT

General Requirements:

Specifier Note: Paragraph below should list obligations for compliance with specific code requirements particular to this section. General statements to comply with a particular code are typically addressed in Contract Conditions and Section 01 41 00 - Regulatory Requirements. Repetitive statements should be avoided.

Regulatory Requirements:

In accordance with Section [01 41 00 - Regulatory Requirements].

[______].

Compatibility:

Verify that components and materials are compatible with specified accessories and adjacent materials.

Electrical Controls: Provide the following:

Switch: Wall mounted 3 position type with cover plate for UP, DOWN and STOP functions.

Materials: Provide motorized projector mount constructed of the following:

Frame: Welded steel, with two 120 VAC grounded electrical outlets to power projector furnished on the platform and removable tray attached to bottom frame assembly.

Grooved Coupling: 1 1/2 inch (38.1 mm) NPT steel half pipe.

U-Joint, Legs: 14 gauge formed steel.

Pitch Bracket, Locking Ring, Base Disk: 11 gauge steel.

Specifier Note: Specify finish of frame bottom to suit project requirements.

Bottom Finish: Powder coated [white] [to match ceiling].

Electrical Requirements: Provide the following:

Specifier Note: Non-pivot type motorized projector lifts by Da-Lite Screen Co., Inc., are available with a number of accessories. Refer to manufacturer’s product and technical information and retain or delete paragraphs below. Edit bracketed information to suit project requirements.

Accessories:

External Single Motor Low Voltage Control (LVC) System:

Specifier Note: Specify wireless remote control with either radio frequency or infrared operation to suit project requirements.

Wireless Remote Control for LVC: [Radio frequency remote [with frequency range extender]] [Infrared] 3-button handheld remote control for UP, DOWN and STOP functions with single motor, low voltage control unit.

Key Locking Cover Plate: Provide hinged cover plate with brushed stainless steel finish provides keyed access to [120 V] [LVC] wall switch.

Specifier Note: Key operated switch cannot be used with low voltage control unit.

Key Operated Switch for 120V Only: Flush mounted wall control with white cover plate, key activated for security.

Specifier Note: Specify Video Projector Interface Control to raise or lower projection screen automatically when projector is turned ON or OFF. A projector must have a 5 V - 12 V output to operate the interface.

Video Projector Interface Control: External DC controls and low voltage 3-button switch with cover plate for wall switch operation.

Specifier Note: Retain bracketed information below to specify NET-100 Ethernet-Serial Adapter.

SCB-100 RS-232 Serial Control Board: External [and with NET-100 Ethernet-Serial Adapter].

Plenum Kit:

Specifier Note: Refer to manufacturer’s product and technical information and specify plenum kit model and description to suit project requirements.

Model, Description: [______] [as recommended by manufacturer].

Specifier Note: Non-pivot type concealed motorized projector lifts by Da-Lite Screen Co., Inc., are available in five standard models corresponding to different lengths of travel. Refer to manufacturer’s product information and technical data, and retain or delete paragraph(s) below to suit project requirements.

Da-Lift Motorized Projector Lift Model 10M:

Outside Dimensions:

Width: 22 5/8 inches (575 mm).

Height: 15 inches (381 mm).

Depth: 22 inches (559 mm).

Travel: 10 inches (254 mm).

Inside Dimensions:

Width: 18 1/2 inches (978 mm).

Height Range to Accommodate Projector: 10 inches - 17 inches (254 - 432 mm).

Depth: 17 1/2 inches (445 mm).

Unit Weight: 87 lb (39 kg).

Performance Criteria:

Capacity: To 40 lb (18 kg), maximum.

UL and ULC listed.

Operation: Provide the following:

Drive: Rack and pinion with chain.

Motor: Three-wire with ground, quick reversal type, oiled for life, with automatic thermal overload cutout, integral gears, capacitor and an electric brake to prevent coasting.

Specifier Note: 120 V, 60 Hz operation is standard; 220/240 V, 50 Hz operation is optional. Retain voltage, frequency to suit project requirements.

Voltage, Frequency: [120 V, 60 Hz] [220/240 V, 50 Hz].

Amperage: 1.5, maximum.

Da-Lift Motorized Projector Lift Model 15M:

Outside Dimensions:

Width: 22 5/8 inches (575 mm).

Height: 20 inches (508 mm).

Depth: 22 inches (559 mm).

Travel: 15 inches (381 mm).

Inside Dimensions:

Width: 18 1/2 inches (978 mm).

Height Range to Accommodate Projector: 15 inches - 22 inches (381 - 559 mm).

Depth: 17 1/2 inches (445 mm).

Unit Weight: 87 lb (39 kg).

Performance Criteria:

Capacity: To 40 lb (18 kg), maximum.

UL and ULC listed.

Operation: Provide the following:

Drive: Rack and pinion with chain.

Motor: Three-wire with ground, quick reversal type, oiled for life, with automatic thermal overload cutout, integral gears, capacitor and an electric brake to prevent coasting.

Specifier Note: 120 V, 60 Hz operation is standard; 220/240 V, 50 Hz operation is optional. Retain voltage, frequency to suit project requirements.

Voltage, Frequency: [120 V, 60 Hz] [220/240 V, 50 Hz].

Amperage: 1.5, maximum.

Da-Lift Motorized Projector Lift Model 15:

Outside Dimensions:

Width: 30 3/4 inches (781 mm).

Height: 20 inches (508 mm).

Depth: 34 inches (864 mm).

Travel: 15 inches (381 mm).

Inside Dimensions:

Width: 26 1/2 inches (673 mm).

Height Range to Accommodate Projector: 15 inches - 22 inches (381 - 559 mm).

Depth: 28 1/2 inches (724 mm).

Unit Weight: 122 lb (55 kg).

Performance Criteria:

Capacity: To 300 lb (136 kg), maximum.

UL and ULC listed.

Operation: Provide the following:

Drive: Rack and pinion with chain.

Motor: Three-wire with ground, quick reversal type, oiled for life, with automatic thermal overload cutout, integral gears, capacitor and an electric brake to prevent coasting.

Specifier Note: 120 V, 60 Hz operation is standard; 220/240 V, 50 Hz operation is optional. Retain voltage, frequency to suit project requirements.

Voltage, Frequency: [120 V, 60 Hz] [220/240 V, 50 Hz].

Amperage: 2.2, maximum.

Da-Lift Motorized Projector Lift Model 19:

Outside Dimensions:

Width: 32 3/4 inches (832 mm).

Height: 24 inches (610 mm).

Depth: 38 inches (965 mm).

Travel: 19 inches (483 mm).

Inside Dimensions:

Width: 28 1/2 inches (724 mm).

Height Range to Accommodate Projector: 19 inches - 30 inches (483 - 762 mm).

Depth: 32 1/2 inches (826 mm).

Unit Weight: 132 lb (60 kg).

Performance Criteria:

Capacity: To 300 lb (136 kg), maximum.

UL and ULC listed.

Operation: Provide the following:

Drive: Rack and pinion with chain.

Motor: Three-wire with ground, quick reversal type, oiled for life, with automatic thermal overload cutout, integral gears, capacitor and an electric brake to prevent coasting.

Specifier Note: 120 V, 60 Hz operation is standard; 220/240 V, 50 Hz operation is optional. Retain voltage, frequency to suit project requirements.

Voltage, Frequency: [120 V, 60 Hz] [220/240 V, 50 Hz].

Amperage: 2.2, maximum.

Da-Lift Motorized Projector Lift Model 19L:

Outside Dimensions:

Width: 42 3/4 inches (1086 mm).

Height: 24 inches (610 mm).

Depth: 48 inches (1219 mm).

Travel: 19 inches (483 mm).

Inside Dimensions:

Width: 38 1/2 inches (978 mm).

Height Range to Accommodate Projector: 19 inches - 30 inches (483 - 762 mm).

Depth: 42 1/2 inches (1080 mm).

Unit Weight: 177 lb (80 kg).

Performance Criteria:

Capacity: To 300 lb (136 kg), maximum.

UL and ULC listed.

Operation: Provide the following:

Drive: Rack and pinion with chain.

Motor: Three-wire with ground, quick reversal type, oiled for life, with automatic thermal overload cutout, integral gears, capacitor and an electric brake to prevent coasting.

Specifier Note: 120 V, 60 Hz operation is standard; 220/240 V, 50 Hz operation is optional. Retain voltage, frequency to suit project requirements.

Voltage, Frequency: [120 V, 60 Hz] [220/240 V, 50 Hz].

Amperage: 2.2, maximum.

EXECUTION

EXAMINATION

Verification of Conditions: Verify that conditions of substrates previously installed under other sections or contracts are acceptable for product installation in accordance with manufacturer(s instructions prior to motorized projector lift installation.

Inform [Owner] [Architect] [Consultant] [______] of unacceptable conditions immediately upon discovery.

Proceed with installation only after unacceptable conditions have been remedied.

Verify that electrical power supply is installed to meet electric projection screen requirements in accordance with Section [26 05 00 - Common Work Results for Electrical].

Verify type and location of power supply.

PREPARATION

Verify that mounting surface is capable of supporting a static load of four times the combined weight of the projector and the mount.

Remove projector lift assembly contents from carton and verify that there are no damaged or missing parts.

Specifier Note: Specify actions required to prepare the surface, area or site for incorporation of the section’s primary products.

Surface Preparation: Prepare [surface] [area] [site] in accordance with manufacturer(s written recommendations and coordinate with Section [01 71 00 - Examination and Preparation].

[______].

INSTALLATION

Coordinate installation of motorized projector lift in accordance with Section [01 73 19 - Installation], manufacturer’s installation instructions and reviewed shop drawings at locations and heights indicated.

Coordinate motorized projector lift work with work of other trades for proper time and sequence to avoid construction delays.

Install motorized projector lift plumb and level to supporting substrate.

Accurately fit, align, securely fasten and install free from distortion or defects.

[______].

FIELD QUALITY CONTROL

Specifier Note: Specify requirements if manufacturers are to provide field quality control with onsite personnel for instruction or supervision of product installation, application, erection or construction. Manufacturers’ field reports are included under PART 1, Submittals.

    - Manufacturer Services:

Specifier Note: Use the following Subparagraphs only when manufacturer(s field services are provided and are required to verify the quality of the installed components. Establish the number and duration of periodic site visits required by manufacturer and specify below. Consult manufacturer for services required. Delete if field services are not required.

      - Coordinate manufacturer(s services with Section [01 45 00 - Quality Control]. Have manufacturer review work involved in handling, installation/application, protection and cleaning of product[s], and submit written reports in acceptable format to verify compliance of work with Contract.

      - Manufacturer(s Field Services: Provide manufacturer(s field services consisting of product use recommendations and periodic site visits for product installation inspection in accordance with manufacturer(s instructions.

      - Schedule site visits to review work at stages listed:

        - After delivery and storage of products, and when preparatory work on which work of this Section depends is complete, but before installation begins.

        - [Twice] during progress of work at [25%] and [60%] complete.

        - Upon completion of work, after cleaning is carried out.

      - Obtain reports within [three] days of review and submit immediately to [Owner] [Architect] [Consultant].

Specifier Note: Specify final actions required to prepare installed products to perform properly. Only include the following Article when installation includes control settings or movable parts.

ADJUSTING

Adjust components and systems for correct function and operation in accordance with manufacturer(s written instructions. Coordinate with Section [01 75 00 - Starting and Adjusting].

Verify controls, limit switches and other components function as designed and meet project requirements.

Adjust motors, controls and components to allow for smooth, unobstructed operation.

[______].

CLEANING

Perform cleanup in accordance with Section [01 74 00 - Cleaning and Waste Management] and Section [01 74 13 - Progress Cleaning].

Upon completion, remove surplus materials, rubbish, tools and equipment in accordance with Section [01 74 23 - Final Cleaning].

Specifier Note: Specify special measures needed to minimize waste, collect recyclable waste and dispose of or recycle field-generated construction waste created during demolition, construction or final cleaning.

Waste Management:

Coordinate recycling of waste materials with Section [01 74 19 - Construction Waste Management and Disposal].

Collect recyclable waste and dispose of or recycle field generated construction waste created during demolition, construction or final cleaning.

Remove recycling containers and bins from site.

[______].

Specifier Note: Coordinate the following Article with Section 01 76 00 - Protecting Installed Construction.

  - PROTECTION

    - Protect installed product from damage during construction in accordance with Section [01 76 00 - Protecting Installed Construction].

    - Repair damage to adjacent materials caused by motorized projector lift installation.

    - [______].

Specifier Note: Specify attachments such as schedules, tables, illustrations or forms in this location if they are not incorporated directly within the specification text.

  - ATTACHMENTS

Specifier Note: Schedules are sometimes placed in the specifications rather than on the drawings. Include schedules that indicate item/element/product/equipment, location and other coordinating data.

    - Schedules:

      - [______].

END OF SECTION